## Slide 1: session2

## Slide 2
A Local Area Network (LAN) is a network that connects computers and devices within a limited geographical area, such as a home, office, or campus.
LANs typically consist of several components that work together to facilitate communication and data sharing among connected devices.

## Slide 3: components of a LAN :
Computers and Devices: Computers, laptops, smartphones, tablets, printers, scanners, servers, and other network-enabled devices are the endpoints or nodes connected to the LAN.
Network Interface Cards (NICs): Network Interface Cards (NICs) are hardware components installed in computers and devices to enable them to connect to the LAN.
NICs provide the physical interface for connecting devices to the network, typically using Ethernet cables or wireless connections (Wi-Fi).

## Slide 4
Switches: Switches are networking devices that serve as the central point of connection for devices within the LAN.
Switches use MAC addresses to forward data packets between devices on the same network, providing efficient and direct communication between devices.
Router: Routers are networking devices that connect multiple LANs together or connect LANs to wider networks such as the internet.
Routers forward data packets between different networks based on IP addresses, allowing devices on the LAN to communicate with devices on other networks.

## Slide 5
Cables and Connectors: Ethernet cables, such as twisted-pair copper cables (e.g., Cat 5e, Cat 6) or fiber optic cables, are used to physically connect devices to the LAN infrastructure.
Connectors such as RJ45 connectors are used to terminate Ethernet cables and connect them to devices and networking equipment.
Wireless Access Points (WAPs): networking devices that provide wireless connectivity to devices within the LAN.
WAPs transmit and receive data wirelessly using Wi-Fi technology, allowing devices such as laptops, smartphones, and tablets to connect to the LAN without requiring physical cables.

## Slide 6
LAN Protocols and Standards: LANs use various protocols and standards to enable communication and data exchange between devices.
Common LAN protocols include Ethernet, Wi-Fi (IEEE 802.11), TCP/IP, and others.
Standards organizations such as the Institute of Electrical and Electronics Engineers (IEEE) define specifications for LAN technologies.
Network Operating System (NOS): software that manages network resources and services within the LAN.
provide functionalities such as file sharing, printer sharing, user authentication, and network administration tools to facilitate network management and operations.

## Slide 7
Network Infrastructure: all the physical and logical components that make up the LAN, including switches, routers, cables, wireless access points, and network management software.
Security Measures: Security measures such as firewalls, intrusion detection/prevention systems (IDS/IPS), access controls, and encryption protocols are implemented to protect the LAN from unauthorized access, data breaches, and cyber threats.
These security measures help ensure the confidentiality, integrity, and availability of data on the LAN.

## Slide 8: These components work together to create a functional LAN
Node:
any device or data point on a network.
it can include computers, servers, printers, routers, switches, or any other network-enabled device.
Each node on a network has a unique identifier, such as a MAC address or IP address, which allows it to communicate and exchange data with other nodes on the network.
Nodes may act as both senders and receivers of data, and they participate in the routing and delivery of data packets across the network.

## Slide 9
NIC (Network Interface Card):
hardware component installed in a computer or other device that enables it to connect to a network.
provide the physical interface for connecting devices to the network infrastructure, typically using Ethernet cables for wired connections or wireless technology (such as Wi-Fi) for wireless connections.
responsible for transmitting and receiving data packets over the network, and they may support various network protocols and communication standards.
have a unique identifier called a MAC address, which is used to identify the device on the network.

## Slide 10
Modem:
A modem (modulator-demodulator) is a networking device that converts digital signals from a computer or network into analog signals that can be transmitted over a communication channel (such as a telephone line or cable line), and vice versa.
used to establish connections to the internet or other wide area networks (WANs) over existing communication infrastructure, such as telephone lines (for dial-up modems), cable lines (for cable modems), or fiber optic lines (for fiber optic modems).

## Slide 11
modems may support various communication standards and protocols, such as DSL, cable, fiber optic, or satellite.
modems may also perform other functions such as modulation/demodulation, error correction, data compression, and protocol conversion.
provided by internet service providers (ISPs) to customers as part of their internet service package, and they are typically connected to the customer's computer or network router to provide internet access.

## Slide 12
An Access Point (AP) is a networking device that allows wireless devices, such as laptops, smartphones, tablets, and IoT devices, to connect to a wired network.
used in Wi-Fi networks to provide wireless connectivity and access to network resources.
key points about access points:
Wireless Connectivity: create a wireless local area network (WLAN) by broadcasting Wi-Fi signals, allowing wireless devices within range to connect to the network.

## Slide 13
Bridge Between Wired and Wireless Networks: Access points act as a bridge between the wired network infrastructure, such as Ethernet switches or routers, and wireless devices.
They facilitate communication and data exchange between wired and wireless devices on the network.
Coverage Area: Access points have a specific coverage area or range within which wireless devices can connect to the network.
The coverage area depends on factors such as the transmit power of the access point, antenna configuration, and environmental conditions.

## Slide 14
SSID: Each access point broadcasts a Service Set Identifier (SSID), which is a unique identifier for the wireless network.
Users can search for available networks and connect to the desired SSID to access the network provided by the access point.
PoE Support: support Power over Ethernet (PoE), allowing them to receive power and data over a single Ethernet cable.

## Slide 15
Authentication and Encryption: support authentication and encryption mechanisms to secure the wireless network.
Common security protocols include Wi-Fi Protected Access (WPA) and WPA2, which use techniques such as pre-shared keys (PSKs) or enterprise authentication (e.g., 802.1X) to authenticate users and encrypt data.
Management and Configuration: managed and configured using management interfaces such as web-based administration consoles or dedicated management software.
Administrators can configure settings such as network name (SSID), security settings, channel selection, and quality of service (QoS) parameters.

## Slide 16
Multiple Access Points: In larger environments or areas with high user density, multiple access points may be deployed to provide seamless coverage and distribute network traffic more evenly.
Access points can be configured to work together in a coordinated manner, forming a wireless network infrastructure known as a wireless LAN (WLAN) or Wi-Fi network.

## Slide 17: A hub
A hub is a basic networking device that serves as a central connection point for multiple devices in a local area network (LAN).
It receives data packets from one device and broadcasts them to all other connected devices.
There are two main types of hubs: active hubs and passive hubs.

## Slide 18: Active Hub:
also known as a "multi-port repeater," regenerates and amplifies incoming data signals before forwarding them to all other ports.
require a power source to operate because they actively regenerate and amplify signals.
have multiple ports, allowing multiple devices to connect to the LAN.
inexpensive and straightforward devices, making them suitable for small LANs or temporary network setups.
not commonly used in modern networking environments due to their limitations compared to more advanced networking devices like switches.

## Slide 19: Passive Hub:
also known as a "dumb hub" or "concentrator," simply serves as a physical connection point for devices without performing any signal regeneration or amplification.
do not require a power source because they do not actively regenerate or amplify signals.
They rely on the electrical properties of the connected cables to transmit data between devices.

## Slide 20
All data packets received by a passive hub are broadcast to all other connected devices, regardless of the intended recipient.
lead to network congestion and reduced performance, especially in larger networks.
rarely used in modern networking environments due to their limitations in terms of performance, scalability, and network management.

## Slide 21
Ethernet switches have largely replaced passive hubs in LANs because they offer improved performance, better management capabilities, and support for features such as VLANs, Quality of Service (QoS), and port mirroring.

## Slide 22: REPEATERS:
networking device that receives a signal, cleans it of any noise or interference, and then regenerates and retransmits the signal to extend the reach of the network.
used to overcome the limitations of signal attenuation, which occurs when signals weaken as they travel over long distances through network cables.
operate at the physical layer (Layer 1) of the OSI model and are transparent to the higher layers of the network protocol stack.

## Slide 23
They do not make any decisions about the data they receive;
they simply amplify and forward the signals they receive.
often used in Ethernet networks to extend the maximum distance between network devices, such as computers and switches, beyond the standard Ethernet cable length limit of 100 meters.
repeaters have limitations in terms of their ability to improve network performance, as they do not segment or filter network traffic.

## Slide 24: Bridges:
A bridge is a networking device that connects two or more network segments or LANs, allowing them to communicate with each other while keeping traffic separate and contained within each segment.
operate at the data link layer (Layer 2) of the OSI model and make forwarding decisions based on the MAC addresses of devices connected to the network.

## Slide 25
Bridges use a process called filtering to selectively forward network traffic only to the segment where the destination device is located, reducing unnecessary traffic on the network.
bridges help improve network performance, reduce collisions, and increase available bandwidth within each network segment.
used to connect different physical or logical LAN segments, such as Ethernet segments, and to divide large LANs into smaller, more manageable segments.

## Slide 26
Modern bridges are often integrated into Ethernet switches, which provide additional features such as VLAN support, port-based security, and Quality of Service (QoS) capabilities.
In summary, repeaters are used to extend the reach of a network by regenerating and retransmitting signals, while bridges are used to connect and segment network segments or LANs, improving performance and reducing network congestion.
bridges offer more advanced features for controlling and managing network traffic.

## Slide 27: SWITCH:
used to connect multiple devices within a local area network (LAN).
Switches use MAC addresses to forward data packets between devices on the same network.
They maintain a MAC address table, also known as a forwarding table or CAM table, which maps MAC addresses to the physical ports on the switch.
When a data packet arrives at a switch, the switch examines the destination MAC address and forwards the packet only to the port where the destination device is located, improving network efficiency and reducing unnecessary traffic.

## Slide 28
Switches are capable of full-duplex communication, allowing devices to transmit and receive data simultaneously on separate channels, which enhances network performance.
Managed switches offer additional features such as VLAN support, Quality of Service (QoS) prioritization, port mirroring, and link aggregation, providing greater flexibility and control over network traffic.

## Slide 29: Router:
operates at the network layer (Layer 3) of the OSI model.
used to connect multiple networks together, such as LANs, WANs, or the internet.
Routers use IP addresses to forward data packets between networks based on routing tables, which contain information about the best paths and next-hop destinations for routing traffic.
When a data packet arrives at a router, the router examines the destination IP address and determines the best path to forward the packet to its destination network.
Routers are responsible for making decisions about how to route data between different networks.

## Slide 30
Routers provide functions such as packet forwarding, routing, and network address translation (NAT), which allows multiple devices on a LAN to share a single public IP address for internet access.
offer additional features such as firewall capabilities, VPN support, bandwidth management, and intrusion detection/prevention systems (IDS/IPS), providing enhanced security and network management capabilities.

## Slide 31: Network cable connectors
used to terminate network cables and establish connections between networking devices, such as computers, switches, routers, and access points.

## Slide 32: TYPES OF NETWORK CABLE CONNECTORS
RJ45 Connector:
The RJ45 connector is the most common type of connector used for Ethernet cables, including Cat5e, Cat6, and Cat6a cables.
It has eight pins that correspond to eight wires inside the Ethernet cable.
used with twisted-pair copper cables and are used for both wired Ethernet connections and for terminating cables to connect to devices such as computers, switches, routers, and access points.

## Slide 33
RJ11 Connector:
used for telephone cables and is similar in appearance to the RJ45 connector but smaller.
It has four or six pins and is used for terminating telephone cables for connecting landline telephones, fax machines, and DSL modems.
F-Type Connector:
used for coaxial cables, primarily in cable television (CATV) and satellite TV installations.
used to connect cable modems, satellite receivers, and cable TV boxes to the coaxial cable infrastructure.

## Slide 34
BNC Connector:
The BNC (Bayonet Neill-Concelman) connector is used for coaxial cables and is commonly used in video and RF applications, such as CCTV cameras and networking equipment.
It features a twist-lock mechanism for secure connections and is commonly used for connecting thin Ethernet (10BASE2) and thick Ethernet (10BASE5) cables.

## Slide 35
LC Connector:
small form-factor fiber optic connector commonly used in data communication and telecommunications networks.
It features a push-pull mechanism for easy insertion and removal and is used with small diameter single-mode or multimode fiber optic cables.

## Slide 36
SC Connector:
The SC (Subscriber Connector) connector is another type of fiber optic connector commonly used in networking applications.
It features a push-pull coupling mechanism and is commonly used with multimode and single-mode fiber optic cables for high-speed data transmission.

## Slide 37
ST Connector:
The ST (Straight Tip) connector is an older type of fiber optic connector that was commonly used in networking and telecommunications applications.
It features a bayonet-style coupling mechanism and is used with multimode fiber optic cables for data transmission.